## Slide 1: November research training trip
George Wadsworth

## Slide 2: What I knew
Theoretical understanding of cell culture
Basic knowledge of the µ-SiM device and its uses
Undergraduate theoretical knowledge of high-end microscopy
Sterile manufacture of µ-SiM devices
Basic cell culture technique and correct use of BSC’s
Cell culture protocols on the devices, specifically co-culture
Application of microscopy techniques to devices
What I needed to learn
Pre-visit
Notes: The practice of cell culture techniques was not a part of Neuroscience UG degree and there was also the impact of the pandemic.
The aims on the right were discussed by myself, Kevin, and Jim before/at the very start of the visit.

## Slide 3
Arrival – 1st November
Week 1 – cell culture basics?
Week 2 – device handling?
Week 3 – co-culture?
Departure – 29th November
Total of only 17 working days at UR, with main goal being co-culture

## Slide 4: Skills – cell culture
Confident with the basics of cell culture:
  Thawing
  Seeding
  Growing to confluence
  Splitting and cell count
  Freezing
Developing the “muscle memory” for safe BSC usage
Aseptic technique
Notes: Prior to the trip, I had no practical cell culture experience, only inductions from the BDI and Kerry.
Therefore, I had Julie from Rochester go over the basics with me, helped me with aseptic technique as it takes a while to get comfortable with the setup of a BSC and to develop the mindfulness of maintaining aseptic technique.
Now I feel competent and somewhat autonomous with the cell culture process, should not take me long to get setup with the cell culture labs in life sciences and at the BDI.
Bullet point all steps of cell culture – from cryo to popoulated devices

## Slide 5: The modular µ-SiM
500 nm
adapted from [1].
adapted from [2].
[1] A. van den Berg and M. Wessling, Nature, 2007.
[2] M. Dehghani, et al., Advanced Materials Technologies, 2019
Notes: Very kindly was sent these diagrams for Kevin Ling, one of the grad students in Jim’s lab.
The top left is the standard set up of the device, an ideal platform for modelling barrier tissues. During my time, I observed the many ways that the McGrath group was utilising the modular aspect of this system. Some examples include inserts for TEER measurement, multi top well inserts, multi-channel bottom layers, flow inserts. Many different compartmental barrier tissue models, with the aim of better replicating human barrier tissues such as the BBB, BRB, hToC, etc.
A – shows the nanoscale modules that make up the conventional ultrafiltration membrane that form a significant restriction to flow. B – the ultrathin porous nanocrystalline membranes that allow efficient protein separation without restricting the flow as much.
2 – SEM images showing the thinness and high porosity of NPN.

## Slide 6: Skills – device preparation and cell culturing
Ability to assemble devices sterilely, and successfully, in a BSC
Knowledge of how to prepare devices for cell culture
Become familiar with the protocol of co-culture
More importantly: the tips and tricks that aren’t in the papers
  Everyone in the McGrath lab had their own techniques
  The best ways to assemble devices
  Handling the devices with hose clamps
  Don’t UV the hose clamps!
  Bubble prevention and removal
  Tilting devices when pipetting bottom channel
  Checking for bubbles in the pipette ports
  Handling micropipettes safely
  Best way to organise devices in BSC and petri dishes (to reduce contamination)
  Etc.
Notes: Device assembly takes patience and practice, the cell culture protocols have been developed and constantly adapted by the McGrath lab, and I’m sure the users in the BDI also have their own protocols.
There are some many specific tips and tricks with all aspects of using these devices, little things such as the different methods for keeping the devices hydrated, tips on how to more effectively assemble said devices, precautions to not break the devices when handling them, and how to avoid and deal with bubbles.

## Slide 7: Co-culture – 1st attempt
HUVEC cell seeding, bottom channel only
Cultures appear more complex following seeding of both sides of the membrane
Top well seeded
Device 1
Device 1
Device 2
Device 2
Notes: My culture practice was with the HUVEC cell line (endothelial cell line isolated from the vein of the umbilical cord), this was chosen as it is a very forgiving cell culture line to work with and the protocols for culturing HUVEC cells onto the devices are very well practiced in the McGrath lab.
On the left are the more successful phase images, but you can observe a different in seeding density. I am aware of the steps that can be taken to avoid this, it’s as simple as regularly mixing your cells solution to try ensure each device receives cells are the same density.
On the left there are some examples of some issues, the first image and third image show that some form of debris and got into the devices. The grad students in Jim’s weren’t too sure what this was, I would put it down to poor aseptic technique from myself as these images were from my first attempt at culturing on the devices. The middle image is an example of the bottom channel having a bubble trapped inside, and this can result in the cells being easily washed away.

## Slide 8: Co-culture – 1st attempt
Here we have 4 different devices, with these phase images in sequence
Observe the influence of progressive meniscus formation via evaporation across the devices
This evaporation can not only affect microscopy quality (out of phase images), but means these devices need daily attention
Notes: On the left, you can clearly see how the phase images become substantially more complex when the top of the membrane is seeded as well.
On the right, the first image I believe is what images look like when the microscope is out of phase and not aligned properly. Also, you can also see how bubbles in the bottom channel can be catastrophic.
Time passing from left to right, showing influence of the menisucus, progressive formation via evaporation, Ewan HULA will fix this, not sure that these were all in sequence, discuss with Kevin

## Slide 9: Co-culture 1 – day 4, I came here to make mistakes
Notes: Contaminated device has been fixed. Obvious that there was contamination due to the cloudy top well media and the process of fungi-like projections? (find the proper name)
Made me review my aseptic technique, little details such as aliquoting off a portion of your media to ensure to do you contaminate a whole tube of media. I also believe that I need to take more care when exchanging media onto the devices, ensuring that I keep my hands and fingers as far away as possible.
The most likely reason for the death is that I did not exchange media over the weekend, the devices are not flasks. The volume is media is so much smaller, the pH and metabolic waste will build up so quicker. Therefore, the media needs to be exchanged ideally every day, and only left for a maximum of one day to avoid cell death. Also, on the left, the final image has the rounded edges, this is due to a bubble being stuck in the trench of the membrane chip when the device has a trench down configuration.

## Slide 10: Co-culture – lessons learnt
HUVEC cells seeding into the bottom channel
Large scratches from bottom of the devices
Care must be taken when ensuring bottom channel (component 2) in properly adhered to component 1
Notes: Image from co-culture 3 – bottom channel only

## Slide 11: Co-culture – lessons learnt
DAY 1
DAY 2
HUVEC cell co-culture
Bubbles must be avoided wherever possible
Even though bubble was successfully removed by day 2, the impact is clear
Notes: Images from co-culture 3

## Slide 12: Co-culture – lessons learnt
HUVEC cell culture, bottom channel only
These are different devices, meant to be seeded at the same density
The vast difference in seeding density, down to not mixing the cell solution regularly whilst seeding multiple devices.
Notes: Images from co-culture 3

## Slide 13
DAY 1
DAY 2
HUVEC-HUVEC co-cultures, attempt 2
Confluent cultures by day 2
Devices used for IHC, basement membrane stain

## Slide 14: Basement membrane staining
3D view of HUVEC-HUVEC co-culture
Antibodies:
  Mouse Anti-Human Collagen type IV, Alexa Fluor 647
  Mouse Anti-Human Fibronectin, Fluor 488
  Rabbit Anti-Human Laminin Goat Anti-Rabbit Alexa Fluor 568
  Hoechst nuclear stain
Gap in cell layers – seeding on top of membrane and bottom channel
Notes: Antibodies –
Mouse Anti-Human Collagen Type IV, Alexa Fluor 647 Mouse Anti-Human Fibronectin, Alexa Fluor 488
Rabbit Anti-Human Laminin, Goat Anti-Rabbit Alexa Fluor 568
Hoechst nuclear stain (405 DAPI on Imaris)
As well as showing the overlay, show the separate channels, use Image J, split colour channels and, make RGB, Image stack and make montage, have epitope on screen in the relevant colour

## Slide 15: Basement membrane staining
  Mouse Anti-Human Collagen type IV, Alexa Fluor 647
  Mouse Anti-Human Fibronectin, Fluor 488
  Rabbit Anti-Human Laminin Goat Anti-Rabbit Alexa Fluor 568
  Hoechst nuclear stain
Notes: Top of the membrane
Antibodies –
Mouse Anti-Human Collagen Type IV, Alexa Fluor 647 Mouse Anti-Human Fibronectin, Alexa Fluor 488
Rabbit Anti-Human Laminin, Goat Anti-Rabbit Alexa Fluor 568
Hoechst nuclear stain (405 DAPI on Imaris)
As well as showing the overlay, show the separate channels, use Image J, split colour channels and, make RGB, Image stack and make montage, have epitope on screen in the relevant colour

## Slide 16: Basement membrane staining
  Mouse Anti-Human Collagen type IV, Alexa Fluor 647
  Mouse Anti-Human Fibronectin, Fluor 488
  Rabbit Anti-Human Laminin Goat Anti-Rabbit Alexa Fluor 568
  Hoechst nuclear stain
Notes: Bottom channel on the device
Antibodies –
Mouse Anti-Human Collagen Type IV, Alexa Fluor 647 Mouse Anti-Human Fibronectin, Alexa Fluor 488
Rabbit Anti-Human Laminin, Goat Anti-Rabbit Alexa Fluor 568
Hoechst nuclear stain (405 DAPI on Imaris)
As well as showing the overlay, show the separate channels, use Image J, split colour channels and, make RGB, Image stack and make montage, have epitope on screen in the relevant colour

## Slide 17
Arrival – 1st November
Week 1 – cell culture basics?
Week 2 – device handling?
Week 3 – co-culture?
Departure – 29th November
Total of only 17 working days at UR, with main goal being co-culture
These 3 main targets were hit, alongside many others:
Permeability assays and TEER measurements.
IHC techniques, basement membrane stain.
Spinning disk confocal microscopy.
Imaris software
Notes: Also, all the different uses of the devices, flow mimetics, mutli-channel components two, inserts for multiple top wells, etc.
Cut down words heavily
Make outcomes of th etrip title clide

## Slide 18: Wegmaniacs and garbage plates

## Slide 22: What next? Future goals
Short term goals:
Reproduce co-culture, but with blood-retinal barrier and blood-lung barrier models (BDI)
Validate culture of epithelial barriers, with IHC and permeability assays
Begin applying the novel optics and microscopy of OPG
Longer term goals:
Impedance microscopy
Hydrodynamic imaging
TEER measurements at Nottingham
Quantitative-phase imaging
Drug delivery system
Microspheres (much later)
Notes: Jim, I know had mentioned maybe starting with HUVEC to practice some more.
Need an order of devices components and potentially cells.
Microspheres way later